## Slide 1: Portable Rydberg System
Haroldo T. Hattori
01 October 2026

## Slide 2: Original setup

## Slide 3: 1.1 Oversimplified scheme
DLPro 780 nm
Fiberport couple into fiber + fiber collimator
Rubidium
cell
Photodetectors and amplifiers
Fiber collimator+fiber

## Slide 4: Feasibility
After purchase 1 if 10 GHz photoreceiver works
Otherwise, must wait until purchase 3 is fulfilled

## Slide 5: Additional equipment needed
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11B (fiberport) => 689.30 USD
CFC8-B or CFC11P-B (preferrable) (780 nm) – Two (one to collimate and another to collect)
Price:338.29 USD each=> 676.5 USD + posting

## Slide 6: Other
Purchase a new DET025AFC 2 GHz Si FC/PC coupled photodetector 400-1100 nm 359.72 USD

## Slide 7: Initial results 30 September 2026
Fibeport: Input 6.7 mW and 6 mW coupled through fibeport ~89.6% efficiency
400 uW coupling after rubidium cell: 6% efficiency.

## Slide 8: 1.2 Oversimplified scheme HALT
780 nm DBR laser
Fiberport couple into fiber + fiber collimator
Rubidium
cell
Photodetectors and amplifiers
Fiber collimator+fiber

## Slide 9: Additional equipment needed
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11B (fiberport) => 689.30 USD
CFC8-B (780 nm) or CFC11P-B (preferrable)– Two (one to collimate and another to collect)
Price:338.29 USD each=> 676.5 USD + posting
* Thorlabs DBR 780 PN- USD 7202.81

## Slide 10: Other
Purchase a new DET025AFC 2 GHz Si FC/PC coupled photodetector 400-1100 nm 359.72 USD

## Slide 11: 2.1 Complete scheme-> Dirty scheme 1
DLPro 780 nm
Fiberport couple into fiber + fiber collimator
Rubidium
cell
Photodetectors and amplifiers
Fiber collimator+fiber
480 nm DLPro laser
Fiber collimator+fiber

## Slide 12: Feasibility
After purchase 1 if 10 GHz photoreceiver works
Otherwise, must wait until purchase 3 is fulfilled

## Slide 13: Additional equipment needed- 780 branch
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11B (fiberport) => 689.30 USD
CFC8-B (780 nm) or CFC11P-B (preferrable)– – Two (one to collimate and another to collect)
Price:338.29 USD each=> 676.5 USD + posting

## Slide 14: Additional equipment needed- 480 branch
Toptica FOC-MM-480-FCPC
Price:
or
1 CFC11P-A (480 nm) or 2 CPC11P-A (480 nm) if collimated

## Slide 15: 2.2 Complete scheme-> Dirty scheme 2
DLPro 780 nm
Fiberport couple into fiber + fiber collimator
Rubidium
cell
Photodetectors and amplifiers
Fiber collimator+fiber
480 nm DLPro laser
Fiberport couple into fiber +fiber+collimator

## Slide 16: Feasibility
After purchases 1 and 2 if 10 GHz photoreceiver works
Otherwise, must wait until purchase 3 is fulfilled

## Slide 17: Other
Purchase a new DET025AFC 2 GHz Si FC/PC coupled photodetector 400-1100 nm 359.72 USD

## Slide 18: Additional equipment needed- 780 branch
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11B (fiberport) => 689.30 USD
CFC8-B (780 nm) or CFC11P-B (preferrable)– – Two (one to collimate and another to collect)
Price:338.29 USD each=> 676.5 USD + posting

## Slide 19: Additional equipment needed- 480 branch
Toptica FOC-MM-480-FCPC
Price:
or
* PAF 2P- 11A (fiberport) => 689.30 USD

## Slide 20: 2.3 Complete scheme TEMP HALT
780 nm DLPro laser
Fiber collimator
Rubidium
cell
Photodetectors and amplifiers
Fiber coupler
480 nm DLPro laser

## Slide 21: Additional equipment needed- 780 branch
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11B (fiberport) => 689.30 USD
CFC8-B (780 nm) or CFC11P-B (preferrable)– – Two (one to collimate and another to collect)
Price:338.29 USD each=> 676.5 USD + posting

## Slide 22: Additional equipment needed- 480 branch
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11A (fiberport) => 689.30 USD
CFC8-A (480 nm) or CFC11P-A (preferrable)- One
Price:338.29 USD each=> 338.29 USD

## Slide 23: Combined stuff
WDM coupler ???? Chinese companies:
CSRayzer Optical Technology Ltd Haroldo
Flyin optronics co Haroldo
Opto-link corporation Ltd Ishara
Lfiber Optic Limited Ishara
A fiber-pigtailed visible-wavelength dichroic combiner

## Slide 24: 2.4 Complete scheme HALT
780 nm DBR laser
Fiber collimator
Rubidium
cell
Photodetectors and amplifiers
Fiber coupler
480 nm DBR laser

## Slide 25: Additional equipment needed- 780 branch
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11B (fiberport) => 689.30 USD
CFC8-B (780 nm) or CFC11P-B (preferrable)– Two (one to collimate and another to collect)
Price:338.29 USD each=> 676.5 USD + posting
* Thorlabs DBR 780 PN- USD 7202.81

## Slide 26: Additional equipment needed- 480 branch
Toptica FOC-MM-780-FCPC
Price:
or
* PAF 2P- 11A (fiberport) => 689.30 USD
CFC8-A (480 nm) or CFC11P-A (preferrable)- One
Price:338.29 USD each=> 676.5 USD + posting

## Slide 27: Combined stuff
WDM coupler ???? Chinese companies:
CSRayzer Optical Technology Ltd
Flyin optronics co
Opto-link corporation Ltd
Lfiber Optic Limited
A fiber-pigtailed visible-wavelength dichroic combiner

## Slide 28: Phase 1
1. It will take time and money to get a WDM coupler
2. Also, the fiber adaptors will take time
Order fibre adaptors and
Multimode fiber: Thorlabs 50 um diameter multimode OM4
Toptica FOC-MM-780-FCPC
Toptica FOC‑MM‑480‑FCPC
Thorlabs CFC5-A (480 nm) and CFC5-B (780 nm)
Multimode coupler (Chinese company CSRayzer)

## Slide 29: More
If you drop the lab mounts, then the only things you must still add beyond what’s in your slide are:
Enclosure: Metal box + internal plate to bolt: cell, collimators, photodiode, WDM, and fibre adaptors so nothing moves.
Mechanical fixing of optics (non‑lab style): Custom brackets / 3D‑printed holders / small L‑brackets for:
  rubidium cell
  CFC5‑A / CFC5‑B
  photodetector
  WDM coupler
Strain relief & feedthroughs:
  fibre strain relief points
  holes/feedthroughs for fibres and RF cables
  maybe FC bulkhead feedthroughs on the box wall
Compact heater for the cell (if you don’t reuse the bulk one):
  small resistive heater + temperature controller
  thermal insulation around the cell
Everything else in your PPT—lasers, fibre adaptors, OM4, WDM, collimators, detectors, amplifiers—is conceptually complete.
So in portable terms, what’s missing is only:
A box
Simple mechanical fixtures inside it
Strain relief / feedthroughs
A compact cell heater (if you don’t reuse the bulk hardware)
If you want, we can sketch a one‑page mechanical layout for that box so it’s buildable without any optical mounts at all.

## Slide 30: Price list
1. DBR 780 PN- USD 7202.81

## Slide 31: items
Critical missing items
Enclosure + internal mounting plate
Custom brackets / 3D‑printed holders
Fiber strain relief + feedthroughs
Compact heater + temperature controller
WDM coupler specification (not just vendor list)
RF amplifier + power supplies
Cell mounting hardware
Assembly tools & documentation

## Slide 32: Ordered
UNSW -> fulfilled
One (1) CFC11P-A 480 nm
One (1) M116L02 graded index MM OM4 FC/PC and FC/PC
Haroldo
Two (2) CFC11P-B 780 nm
Two (2) M116L02 graded index MM OM4 FC/PC and FC/PC

## Slide 33: Ordered
Haroldo
One (1) CFC11P-A 480 nm
One (1) HCP Post mounting bracket for fiberport
Haroldo
1. One DET025AFC 2 GHz Si FC/PC coupled photodetector 400-1100 nm

## Slide 34: Future purchase
1. One (1) PAF 2P- 11A (fiberport) => 689.30 USD
2. One (1) DET025AFC/M Si biased detector for optical fiber

## Slide 35: Arrived items
Two CFC11P-A (480 nm) have arrived
ONE 2m OM4 fiber patch has arrived
* ONE HCP fiberport holder

## Slide 36: WDM coupler
WDM coupler
780 nm beam
480 nm beam
780 nm beam
480 nm beam